## Slide 1: The LHC accelerator: challenges, achievements and the future
3rd June, Zurich (45mins in total)
Steve Myers
Director of Accelerators and Technology,
CERN

## Slide 2
The Start:
First documented proposal

## Slide 3
S. Myers QUB March 11, 2009
3
Superconducting Proton Accelerator and Collider
installed in a 27km circumference underground tunnel (tunnel cross-section diameter 4m) at CERN
Tunnel was built for LEP collider in 1985
The LHC
Notes: 3

## Slide 4
Total of 9 accelerators at CERN, 12 if you consider the 4 rings of the booster

## Slide 5: Technologies needed for Accelerators and Detectors (some examples)
      Civil engineering (underground caverns and tunnelling...)
      Geodesy (align all components to accuracies not needed in any other domain.)
      Electrical distribution (fast switching and power sharing between Swiss and French networks, network protection, active compensators, susceptibility to electrical storms...)
      Cryogenics (1.9K, superfluid helium, 37Mkg of cold mass, 100 tonnes He. 1260tonnes nitrogen)
      Magnets (9T, twin bore, NbTi sc cable, ~3000 sc magnets + “normal” magnets...)
      Power converters (13kA DC conversion from AC, with 1ppm ripple, resolution,..)
      Ultra High Vacuum (10-9 to 10-11 mbar (Torr) in the presence of beam, 27km)
      Acceleration System (sc RF 400MHz, 1MW klystrons, control of cavities wrt beam)
      Beam Instrumentation (all types of particle detection and control)
      Beam feedback (EM instabilities, detect and stabilize)
      Injection, extraction(high rise time magnetic pulses, PFN, ferrite loaded magnets, UHV)
      Machine protection (10GJ EM stored energy, 720MJ beams energy )
      Targets, dumps and collimators (materials research for particle beams)

## Slide 6: Acceleration (RF) system
S. Myers QUB March 11, 2009
6
Radiofrequency (RF) electric fields
RF cavities are located intermittently along the beam pipe. Each time a beam passes the electric field in an RF cavity, some of the energy from the radio wave is transferred to the particles.
Notes: 6

## Slide 7: In Reality (point 4)
S. Myers QUB March 11, 2009
7
2 Modules per beam
4 Cavities per module
Notes: 7

## Slide 8: Dipole or Bending Magnets
Notes: 8

## Slide 9: If the LHC did not use superconductivity
The LHC has a circumference of 26.7 km, with 20km filled with superconducting magnets operating at 8.3 T. The refrigerators producing the liquid helium to cool the magnets consume 40 MW of power.
An equivalent machine with classical electromagnets would have a circumference of 100 km and would consume 1000 MW of power.

## Slide 10: LHC dipoles (1232 of them) operating at 1.9K
S. Myers QUB March 11, 2009
10
7TeV
8.33T
11850A
7MJ
Contracts by 4.7cm during cool-down
Notes: 10

## Slide 11
Superconducting Dipoles from Recent Colliders

## Slide 12: The LHC tunnel with dipole magnets
beam tubes
Notes: 12

## Slide 13: Interconnections
S. Myers QUB March 11, 2009
During cool-down of the LHC the machine contracts by 80 metres, 10m per octant
  Vacuum continuity
  Electrical connections
Notes: 13

## Slide 14: LHC: Some of the Technical Challenges
Circumference (km) | 26.7 | 100-150m underground
Number of Dipoles | 1232 | Cable Nb-Ti, cold mass 37million kg
Length of Dipole (m) | 14.3 | 
Dipole Field Strength (Tesla) | 8.4 | Results from the high beam energy needed
Operating Temperature (K) | 1.9 | Superconducting magnets needed for the high magnetic field Super-fluid helium
Current in dipole sc coils (A) | 13000 | Results from the high magnetic field 1ppm resolution
Beam Intensity (A) | 0.5 | 2.2.10-6 loss causes quench
Beam Stored Energy (MJoules) | 362 | Results from high beam energy and high beam current 1MJ melts 2kg Cu
Magnet Stored Energy (MJoules)/octant | 1100 | Results from the high magnetic field
Sector Powering Circuit | 8 | 1612 different electrical circuits

## Slide 15: How Much Energy is this?
Energy stored in the magnets 10 GJ (1100 MJ/octant)
Nimitz class aircraft carrier (90 000 tons) at battle-speed of 30 Knots; Energy = ½ mv2 ~ 10GJ
Copper
Melting point 1356 K
Specific heat capacity 386 J kg-1 K-1
Latent heat of fusion 205000 J kg-1
So to heat and melt 1kg takes (1354*386+205000) J =0.73MJ
362MJ could heat and melt half a tonne (500kg) of copper
Energy stored in each beam 362 MJ (in 89us) 4TW (power)
A very thin long hole
In LHC we must dump the magnetic energy in around 40 seconds i.e. stop the aircraft carrier in 40 seconds

## Slide 16: How to Deal with the LHC self Destructive Power
In case of a problem the stored energy in the magnets and in the beam must be transferred to and dissipated in a safe, clearly defined place
Magnet Protection system
  “Quench” Protection (measures resistance)
  Energy dump triggered and energy dissipated as heat in resistors (after of course aborting the beams)
Machine Protection System
  All critical elements which could provoke a beam loss are equipped with an emergency beam abort signal which triggers the beam dump system. There is also a beam loss monitoring system all around the circumference which will abort the beam if anomalous losses occur
  The beam dump system is the last safety net

## Slide 17: LHC beam dump principle (and acronyms)

## Slide 18: Beam dump core (TDE)
7.7m long, 700 mm  graphite core
Graded density of 1.1 g/cm3 and 1.7 g/cm3
12 mm wall, stainless-steel welded pressure vessel, filled with 1.2 bar of N2
Surrounded by ~1000 tonnes of concrete/steel radiation shielding blocks
0.7 m
3.5 m
3.5 m
1.7 g/cm3
1.1 g/cm3
1.7 g/cm3
beam

## Slide 19: Beam dump core with dilution failures
Maximum energy density in dump block
Maximum temperature rise in dump block
Nominal
0/6 vertical diluters
0/4 horizontal diluters
31 kJ/g for onset of sublimation, 60 kJ/g for complete vaporization
Nominal beam intensity (3.21014 p+)

## Slide 20
Collimation

## Slide 21: Collimator settings 2012
Collimation hierarchy has to be respected in order to achieve satisfactory protection and cleaning
 | σ
TCP 7 | 4.3
TCSG 7 | 6.3
TCLA 7 | 8.3
TCSG 6 | 7.1
TCDQ 6 | 7.6
TCT | 9.0
Aperture | 10.5
2012: tight settings

## Slide 22: Collimators (points 3 and 7)
22
56.0 mm
1 mm
Intercept particles that have strayed outside acceptable limits
Notes: 22

## Slide 23
Collimating with small gaps
LHC beam will be physically quite close to collimator material and collimators are long (up to 1.2 m)!

## Slide 24
Damage Level 3 (Catastrophic Damage)
Case 7 (8 bunches at 5 TeV) is the only studied case falling in Damage Level 3.
High probability of water leakage due to very severe plastic deformations on pipes.
Impressive jaw damage :
  Extended eroded and deformed zone.
  Projections of hot and fast solid tungsten bullets (T≈2000K, Vmax ≈ 1 km/s) towards opposite jaw. Slower particles hit tank covers (at velocities just below ballistic limit).
  Risk of “bonding” the two jaws due to the projected resolidified material.
Real Scale Deformations !!
Accident Simulations for TCT

## Slide 25
Damage Level 3 (Catastrophic Damage)
Case 7 (8 bunches at 5 TeV) is the only studied case falling in Damage Level 3.
High probability of water leakage due to very severe plastic deformations on pipes.
Impressive jaw damage :
  Extended eroded and deformed zone.
  Projections of hot and fast solid tungsten bullets (T≈2000K, Vmax ≈ 1 km/s) towards opposite jaw. Slower particles hit tank covers (at velocities just below ballistic limit).
  Risk of “bonding” the two jaws due to the projected resolidified material.
Real Scale Deformations !!
Accident Simulations for TCT

## Slide 26
September 10, 2008; It worked!

## Slide 27: And 9 days later
27
  Making the last step of dipole circuit in sector 34, to 9.3kA
  At 8.7kA, development of resistive zone in the dipole bus bar splice between Q24 R3 and the neighbouring dipole
  Electrical arc developed which punctured the helium enclosure
One inter-magnet connector (out of 100,000) was badly soldered and… The magnet protection system did not protect
Notes: 27

## Slide 28
28
Consequences
Notes: 28

## Slide 29: Electrical arc between C24 and Q24
M3 line
V lines

## Slide 30: Collateral damage: secondary arcs
QQBI.27R3 M3 line
QBBI.B31R3 M3 line

## Slide 31: Bus bar splice
31
Notes: 31

## Slide 32: Fault tree [1/3]
Absence of soldering
Resistance 220 nOhm
Bad contact with stabilizer
No sensitive detection on bus bar
Thermal runaway
Meltdown, open circuit
Power converter fast discharge
Electrical arc
Electro-thermal model
Observed on magnet
What went wrong?

## Slide 33: Fault tree [2/3]
Electrical arc
Beam pipe perforation
He vessel perforation
Soot
He discharge in insulation vacuum
Contamination by soot
Inadequate sizing of relief devices (MCI)
Pressurization of vacuum enclosures
Mechanical damage to MLI
Contamination by MLI
ODH in tunnel
Blast
Trip AUG
Loss of beam vacuum
Break vent door

## Slide 34
+ 8 cryogenics!
But this repair would not allow 14TeV but operation at reduced energy (7-8TeV)

## Slide 35: LHC: First collisions at 7 TeV on 30 March 2010
CMS
ALICE
LHCb

## Slide 36
Performance in 2010

## Slide 37
Integrated Luminosity in 2010
45pb-1 recorded

## Slide 38
Performance in 2011

## Slide 39
Goal 2011
Protons
~ 6000 fb-1

## Slide 40
In 2010:
Peak ~18E24; Integrated ~18ub-1 Max 137 bunches, larger *, smaller bunch intensities
2010
2010
Peak and Integrated luminosity
356 bunches
Ions

## Slide 41
Estimated Luminosity needed for Higgs
October 2011

## Slide 42: 2012 Priorities
The LHC machine must produce enough integrated luminosity to allow ATLAS and CMS to independently discover the Higgs before the start of LS1.
We must also prepare for the proton-lead ion run at the end of the year.
We must (in 2012) do the necessary machine experiments to allow high energy, useful high luminosity running after LS1.

## Slide 43
Performance in 2012

## Slide 44
Integral of all of 2010 now in 2.5 hours
Saturday 2nd June Fill 2692 (238pb-1 in 23 hours)

## Slide 45: Mid 2012: With Respect to estimates
4th July: Melbourne/CERN

## Slide 46: 2012

## Slide 47: Last 3 years

## Slide 48: Tests towards the end of 2012
25 ns tests
    Electron cloud and vacuum (scrubbing)
    Crossing angle, aperture, beam-beam, min β*
    UFOs
    HOM heating
    Short Physics run with Maximum pile up?
Comparison 25 vs 50 ns
    β* levelling testing (already tested in Machine studies)

## Slide 49: FUTURE

## Slide 50: LS1 then operation around 7TeV/beam
LS1 Work
  Repair defectuous interconnects
  Consolidate all interconnects with new design
  Finish off pressure release valves (DN200)
  Bring all necessary equipment up to the level needed for 7TeV/beam

## Slide 51: LHC MB circuit splice consolidation proposal
Phase I
Surfacing of bus bar and installation of redundant shunts by soldering
Phase II
Application of clamp and reinforcement of nearby bus bar insulation
Phase III
Insulation between bus bar and to ground, Lorentz force clamping

## Slide 52: Linear schedule
EDMS 1227656 (rev1.0, July 26th, 2012)
No contingency

## Slide 53
Then operation at 6.5TeV per beam
Assumptions
E=6.5TeV
β* = 0.5m (maybe 0.4)
All other conditions as in 2012 i.e. LHC availability same etc

## Slide 54: Mid-Term Future HL-LHC

## Slide 55: Two Reasons for upgrade: Performance & Technical (Consolidation)
Shut down to fix interconnects and overcome energy limitation (LHC incident of Sept 2008) and R2E
Shut down to overcome beam intensity limitation (Injectors, collimation and more…)
Full upgrade

## Slide 56: Final goal : 3000 fb-1 by 2030’s…
5 1034 levelled lumi (25 1034 virtual peak lumi)
140 pile up (average)
3 fb-1 per day
60% of efficiency
250 fb-1 /year
300 fb-1/year as «ultimate»
Full project
Just continue improving performance through vigorous consolidation

## Slide 57: Official Beam Parameters (see PLC by O.Bruning)
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 2.2E+11 | 3.5E+11
nb | 2808 | 2808 | 1404
beam current [A] | 0.58 | 1.12 | 0.89
x-ing angle [mrad] | 300 | 590 | 590
beam separation [s] | 10 | 12.5 | 11.4
b* [m] | 0.55 | 0.15 | 0.15
en [mm] | 3.75 | 2.5 | 3.0
eL [eVs] | 2.51 | 2.5 | 2.5
energy spread | 1.20E-04 | 1.20E-04 | 1.20E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 80 -> 106 | 20.0 | 20.7
IBS longitudinal [h] | 61 -> 60 | 15.8 | 13.2
Piwinski parameter | 0.68 | 3.1 | 2.9
geom. reduction | 0.83 | 0.35 | 0.33
beam-beam / IP | 3.10E-03 | 3.9E-03 | 5.0E-03
Peak Luminosity | 1 1034 | 7.4 1034 | 8.5 1034
Virtual Luminosity | 1.2 1034 | 21 1034 | 26 1034
(Leveled to 5 1034 cm-2 s-1
and 2.5 1034 cm-2 s-1)
Events / crossing (peak & leveled L) | 19 | 210 | 475 | 140 | 140
6.2 1014 and 4.9 1014
p/beam
sufficient room for leveling
(with Crab Cavities)
Virtual luminosity (25ns) of
L = 7.4 / 0.35 1034 cm-2 s-1
= 21 1034 cm-2 s-1 (‘k’ = 5)
Virtual luminosity (50ns) of
L = 8.5 / 0.33 1034 cm-2 s-1
= 26 1034 cm-2 s-1 (‘k’ = 10)
28

## Slide 58: HiLumi: Two branches (with overlap)
PIC - Performance Improving Consolidation upgrade (1000 fb-1)
  IR quad change (rad. Damage, enhanced cooling)
  Cryogenics (P4, IP4,IP5) separation Arc -RF and IR(?)
  Enhanced Collimation (11T?)
  SC links (in part) and rad. Mitigation (ALARA)
  QPS and Machine Prot.
    Kickers
    Interlock system
FP- Full Performance upgrade (3000 fb-1)
  Crab Cavities
  HB feedback system (SPS)
  Advanced collimation systems
  E-lens (?)
  SC links (all)
  R2E and remote handling for 3000 fb-1

## Slide 59
2022
LS3
Installation of the HL-LHC hardware
Being Reviewed at present

## Slide 60: Long-Term Future: VHE-LHC, e+e-, and ep options

## Slide 61: HE-LHC and VHE-LHC
HE-LHC dipole design will piggy back on the high gradient quadrupole R&D needed for HL-LHC
  Would allow an increase in energy by factor of 2-2.5
VHE-LHC (??SSC) needs a 80-100km tunnel
  In conjunction with the high field magnets would allow a factor of (2-2.5)x(80/27) = 6-7.5 times LHC (42-52 TeV/beam)
This large tunnel would also allow e+e- (TLEP) and e-p collisions as well as pp collisions

## Slide 62: Parameters list of LHC upgrades (O. Dominguez and F. Zimmermann)

## Slide 63
Need to be addressed

## Slide 64: In principle a plan for all (?) is possible (for LHC exploitation): 2018-2020 is critical time
According to Physics needs, the 80-100 km tunnel can:
  Be alternative to HE-LHC
  Or complementary to HE-LHC
  Accomodating at negligible extra-cost TLEP and VLHeC (this last at 50GeV/5TeV and 350 GeV/50-100 TeV)
  Skipping TLEP/VLHeC may shorten 5-10 years VHE-LHC

## Slide 65: Summary
Integrated luminosity goal for 2012 exceeded
“Higgs” discovered
Proton-lead run a big success
LS1 progress is good
Operation after LS1 at 6.5TeV/beam
  25ns much preferred by detectors
Many (ideas) plans for the future!

## Slide 66
Thank you for your attention
2010-2012

## Slide 67: This Ends the Presentation

## Slide 68: Preliminary budget estimate
 | Improving Consolidation | Full performance | Total HL-LHC
Mat. (MCHF) | 476 | 360 | 836
Pers. (MCHF) | 182 | 31 | 213
Pers. (FTE-y) | 910 | 160 | 1070
TOT (MCHF) | 658 | 391 | 1,049

## Slide 69: HE-LHC cost: rough evalution based on LHC
LHC (machine): about 3.4 BCHF, 1.7 BCHF for the magnet system,
HE-LHC: The non-magnet is  same 1.5 BCHF
  Magnet System Nb3Sn (26 TeV c.o.m.) :  3.5 BCHF (for a total of 5 BCHF for the whole machine)
  Magnet System HTS (33 TeV c.o.m) :  5 BCHF (for a total of 6.5 BCHF for the whole machine)
  The above cost are for a new machine, like LHC. Economy could be made because Cryo and other systems need only renovation;
  however one should consider the cost of LHC removal)

## Slide 70: Other important issues (among many …)
Synchrotron radiation
15 to 30 times!
The best is to use a window given by vacuum stability at around 50-60 K (gain a factor 15 in cryopower removal!)
First study on beam impedance seems positive but to be verified carefully
Use of HTS coating on beam screen?
Beam in & out
Both injection and beam dump region are constraints.
Ideally one would need twice stronger kickers
Beam dumps seems feasable by increasing rise time from 3 to 5s
Injection would strongly benefit form stronger kickers otherwise a new lay-out is needed (different with or wihtout experiments)

## Slide 71: Alternate scenarios for Injectors
Keeping SPS (and its transfer lines: 6 km!): Low Energy Ring in LHC tunnel with superferric Pipetron magnets (W. Foster).
Work done by Fermilab (H. Piekarz), see Malta workshop proc.
  cost of LER is lower than SC-SPS option.
  Integration is difficult but no show-stoppers

## Slide 72: Steps for Potential Large Projects beyond the LHC infrastructure: the 47-80 km long ring tunnel
Several proposals exist for major projects at CERN to complement / succeed the LHC
  CLIC, HE-LHC, TLEP, LHeC etc…
Steps to undertake before starting construction planning
  Determine requirements for the project
  Create basic civil engineering drawings
  Perform siting studies
  Perform feasibility studies to determine optimal location
    Optimal is most feasible from civil engineering point of view
  Select optimal location
  Optimize civil engineering drawings according to identified optimal location
J. Osborne

## Slide 73: Possible arrangement in VHE-LHC tunnel
From H. Piekarz Malta Prooc. Pag. 101
30 mm V gap
50 mm H gap
Bin = 0.5 T
Bextr = 1.5 T

## Slide 74: Possible VHE-LHC with a LER suitable also for e+-e- collision (and VLHeC) – 100 MW sr
Advantage:
cheap like resistive magnets
Central gap could be shortcircuited
Magnet separated: provides electron 50 GeV and proton 5 TeV/beam
Limited cryopower (HTS) in shadow of SCRF cavities
Sc cables developed already for SC links (HiLumi) and power application.
SR taken at 300 K: is possible???

## Slide 75: In principle a plan for all (?) is possible (for LHC exploitation): 2018-2020 is critical time
According to Physics needs, the 80 km tunnel can:
  Be alternative to HE-LHC
  Or complementary to HE-LHC
  Accomodating at negligible extra-cost TLEP and VLHeC (this last at 50GeV/5TeV and 350 GeV/50-100 TeV)
  Skipping TLEP/VLHeC may shorten 5-10 years VHE-LHC

## Slide 76: LHC Challenges: R
geometric luminosity
reduction factor:
large crossing angle:
 reduction of long range beam-beam interactions
 reduction of head-on beam-beam parameter
 reduction of the mechanical aperture
 synchro-betatron resonances
 reduction of instantaneous luminosity
 inefficient use of beam current
 option for L leveling!
effective cross section
Piwinski angle
qc

## Slide 77: HL-LHC Performance Goals
Preferred leveling mechanism: Crab Cavities
Reservations: technology & field quality
 Supplementary tools for leveling:
# crossing angle and long-range and
beam-beam wire compensators
# transverse offsets at IP
# dynamic b* squeeze
Operation at performance limit
choose parameters that allow higher than design performance
leveling mechanisms for controlling performance during run

## Slide 78: A >50 Years Adventure The LHC Life cycle
1983: Preliminary Performance Estimates for the LHC (S.Myers and W. Schnell, 11th April 1983)
1984: Kick off meeting to discuss ideas for an accelerator to collide protons at very high energy
1996: Final decision for the LHC, the most complex scientific instrument ever constructed
10 September 2008: Start of commissioning with beam
19 September 2008: Serious incident and damage
19 November 2009: Restart of beam operation
December 2009: first collisions at 2.38 TeV
Today: successful operation, providing millions of particle collisions for the LHC experiments
About 2035: The LHC physics programme to be finished ?

## Slide 81: LHC Status Report
Steve Myers
On behalf of all LHC teams

## Slide 82
Last days of p-p
End of year tests
  25ns and scrubbing
  Quench tests
    Collimation test
    UFOs
    magnets
Lead-proton run + 1.38TeV/beam run, +VDM scans (F
CERN Machine Advisory Ctte (15-16 March)
‘mini-Chamonix (at CERN)’ performance of LIU and HL-LHC
Last Weeks/Months of Run 1 (2009-2013)
Topics

## Slide 83: 2012

## Slide 84: With the modified schedule

## Slide 85: Total Luminosities 2012

## Slide 86: End of Run Tests
High Injector Brightness
End of year tests @ 25ns
  electron cloud and scrubbing
  Quench tests
    Collimation test
    UFOs
    Magnet quench test
    HOM heating

## Slide 87: Injector High Brightness Beams
High brightness beams from the injector chain
  Very interesting option for 2015 operation, both 50 ns and 25 ns beam spacing
Fill with one batch HB and 1 batch ‘standard’ 50 ns
  Emittance for HB beam ~ 1-1.2 um, standard 1.4-1.6 um.
About 30 % gain in specific luminosity !
For 25ns operation, now seems possible 1.15E11 with emittance of 1.4µm at LHC inj.
These and other results provoked the review of the performance of HL-LHC and the needs from LIU

## Slide 88: Beam currents and luminosity
2e14
2.5e14
ATLAS & CMS 7e33 cm-2s-1
LHCb 1e33 cm-2s-1: all holding !
ALICE peak at 10e30 cm-2s-1, level at about 6.5
TDI HB RF TED
25ns scrubbing

## Slide 89: Beam quality evolution
Beam lifetime
Sunday 9 Dec
Friday 7 Dec

## Slide 90: Beam quality evolution (preliminary)
Beam lifetime – Friday Dec. 7th

## Slide 91: Beam quality evolution (preliminary)
Beam lifetime – Saturday Dec. 8th
Thanks to H. Bartosik

## Slide 92: Beam quality evolution (preliminary)
Beam lifetime – Sunday Dec. 9th
Thanks to H. Bartosik

## Slide 93: UFOs

## Slide 94: 25ns Fills
Initially > factor 10 increase in UFO activity with 25ns.
Tendency for conditioning in only 10 fills.
Raw UFO rate
UFO rate normalized to 50ns intensity

## Slide 95: Quench Margin at 7 TeV
Peak energy density in MB coils from FLUKA for largest arc UFO in 2012:
at 3.5TeV: ≈7.8 mJ/cm³ ≈ factor 3 below QP3 quench margin. (T. Baer et al., Evian Workshop 2012)
at 7.0TeV: ≈32.5 mJ/cm³ ≈ factor 5 – 10 (QP3/Note44) above quench margin.
x 4.2
Simulations by A. Lechner and the FLUKA team

## Slide 96: Energy Extrapolation
  Extrapolation to 7 TeV:
  BLM signal/threshold (based on Note44) is for arc UFOs about 20 times larger than at 3.5 TeV.
  Based on 2012 arc UFOs: 91 UFO related beam dumps. (based on 2011: 112 dumps)
  Additionally, 21 beam dumps by MKI UFOs (2012 data, full cycle). (based on 2011: 27 dumps)
Based on the applied threshold table from 10.12.2012. For MKI UFOs, only the BLMs at Q4 and D2 are considered. The energy scaling applies only to events at flat top, but (for MKI UFOs) the full cycle is taken into account for the extrapolation. Apart from the beam energy, identical running conditions as in 2011/2012 are assumed. In particular not included are: margin between BLM thresholds and actual quench limit, 25ns bunch spacing, intensity increase, beam size, scrubbing for arc UFOs, deconditioning after LS1.
For 50ns!

## Slide 97: UFO Quench Test
On 15.02.2013 UFO quench test to verify quench level:
Large orbit bump in arc (MQ.12L6.B2).
Fast beam excitation with tune kicker and transverse damper (inverse sign).
Post analysis ongoing: Geant4, MadX and FLUKA simulations to determine energy density in magnet.
Preliminary estimate: Quench level about a factor 6-13 higher than expected. (not included in analysis on previous slides)
Beam 2
MKQ kick
ADT start
QUENCH! ≈8e8p lost.
10ms

## Slide 98: Summary
21 beam dumps due to UFOs in 2012 (58 dumps since 2010).
Temporal width often < 1 turn (89µs). At higher energy, some events may be too fast for active protection.
Clear conditioning effect of arc UFO rate (≈ factor 5) in 2011/12.
Extrapolation to after LS1:
  25ns: initially >10 times higher arc UFO rate observed, conditioning expected.
  Energy extrapolation to 7TeV: 2012 arc and MKI UFOs would have caused 112 beam dumps (2011: 139).
  First estimates from UFO quench test indicate that quench level estimates may be too pessimistic. (factor of 6-13). Detailed analysis is ongoing.
Mitigations: For Arc UFOs, optimized BLM distribution to allow better UFO protection.
Ndumps  100F25nsFquench  17016 (cf 21 in 2012)
102
0.170.08

## Slide 99: Collimators

## Slide 102: Lead ion Run

## Slide 103: Physics requests for the end of the run
Initial minimum bias p-Pb for ALICE
    L < .05 x 1029 cm-1 s-1, pile up < .003, 4TeV/beam
Integrate 30 nb-1 in ALICE :
  L < 1.0 x 1029 cm-1 s-1; pile up < .05, 4TeV/beam
High luminosity in ATLAS and CMS
Beam reversal p-Pb to Pb-p for ALICE, LHCb
2 ALICE polarity reversals (also LHCb)
Few nb-1 in LHCb (new to heavy-ion operation)
2nd priority: intermediate energy p-p operation; 1.38 TeV/beam
  Integrate 5 nb-1 in ATLAS, CMS

## Slide 104: LHC new features
Unequal revolution frequency injection and ramp
  Potential problems of moving long-range beam-beam kicks (killed this mode of operation of RHIC, was a killer in the ISR)
Frequency-locking, off-momentum operation at top energy, cogging of IPs back to proper positions
New squeeze including ALICE to 0.8 m and LHCb to 2 m
Off-momentum correction of squeeze
Usual, many collimation setups, loss maps in various conditions
Small crossing angle in ALICE (for ZDC)
New filling scheme with collisions of 2 trains in LHCb
  Very close encounters near ALICE

## Slide 105: The Acid Test, 20/1/2013
Fill 3474
First injection and ramp of Pb trains against proton trains
(the MD the team had been trying to do since November 2011).
Conclusion: The moving long-range beam-beam encounters did not cause significant beam losses or emittance blow-up

## Slide 106: Full filling scheme 21st Jan.
Record Pb intensity in LHC !!
Thanks to injectors.

## Slide 107
Monday | 7 | January
Tuesday | 8 | January
Wednesday | 9 | January
Thursday | 10 | January
Friday | 11 | January
Saturday | 12 | January
Sunday | 13 | January
Monday | 14 | January
Tuesday | 15 | January
Wednesday | 16 | January
Thursday | 17 | January
Friday | 18 | January
Saturday | 19 | January
Sunday | 20 | January
Monday | 21 | January
Tuesday | 22 | January
Wednesday | 23 | January
Thursday | 24 | January
Friday | 25 | January
Saturday | 26 | January
Sunday | 27 | January
Monday | 28 | January
Tuesday | 29 | January
Wednesday | 30 | January
Thursday | 31 | January
Friday | 1 | February
Saturday | 2 | February
Sunday | 3 | February
Monday | 4 | February
Tuesday | 5 | February
Wednesday | 6 | February
Thursday | 7 | February
Friday | 8 | February
Saturday | 9 | February
Sunday | 10 | February
Collimation set up, IR2 aperture measurements, first collisions
Restart
First injection in the LHC
Injection checks and Squeeze commissioning
First Stable beams, first injection of trains of p and Pb
End of ALICE minimum bias data taking
ALICE polarity change
Van der Meer scans
Beams reversal
Van der Meer scans
p-Pb
Pb-p
Pb source refill
Run overview
>4 days lost to cryo, power failures

## Slide 108
Luminosity evolution 1/2
Full instantaneous luminosity 1x1029 cm-2.s-1 already reached with the first fill with full filling scheme
Levelling in ALICE at 1x1029 cm-2.s-1 in almost all standard fills
Two fills were done with IP1 and 5 separated, allowing ALICE to catch up after initial minimum-bias
Van der Meer scans done in both configurations
Final integrated luminosity above experiments’ request of 30 nb-1
The run ended with record peak luminosity of 1.15x1029 cm-2.s-1, record turn around of 2.37 h
p-Pb, min. bias
p-Pb
Pb-p
21 Jan 28 Jan 4 Feb Time
p-Pb, min. bias
p-Pb
Pb-p
21 Jan 28 Jan 4 Feb Time

## Slide 109: Summary LHC p-Pb run
A new mode of operation, unforeseen in the baseline design of the LHC, was commissioned in 10 days (including >4 days’ down time).
The physics requirements were fulfilled in both configurations p-Pb and Pb-p in three weeks of physics,
ALICE, ATLAS, CMS, LHCb, ALFA, TOTEM, LHCf all took data.
Fills were routinely dumped by the BPMS false reading
The run gave important data to prepare future high luminosity Pb-Pb and p-Pb runs.

## Slide 110: THE LAST PHYSICS BEAM OF LHC RUN 1 (2009 - 2013)

## Slide 111: Thank you

## Slide 112: HL-LHC LIU Performance Review (8-10 October, CERN)
Review ‘Present’ Performance with 25ns
Review present assumptions (radiation damage) on needed shutdowns
Review present limitations and ‘staged’ upgrades to the injectors and the LHC
For each staged upgrade estimate
  Resources needed (M+P)
  Increase in yearly Integrated luminosity
  Shutdown time needed
Propose optinized machine plan for integrated luminosity and shutdowns till mid 2030s

## Slide 113: Outlook for LHC heavy-ion programme, post-LS1
Prospects of higher performance in p-Pb:
  Usual scalings of geometrical emittance, β* with energy
  Higher p intensity (solve BPM problems, …)
Prospects of higher performance in Pb-Pb:
  Pb injector performance in p-Pb
  Quench limits ?
  Mitigation strategies for DS quenches by BFPP beams from IPs demonstrated in 2011
It will be crucial to define physics priorities and luminosity-levelling strategies !
  Luminosity decay from burn-off will dominate

## Slide 114: Comparison 25ns and 50ns

## Slide 115
Chart: Peak Luminosities (E34)

## Slide 116
Chart: 

## Slide 117
Chart: 

## Slide 118
Chart: Peak Luminosities (E34)

## Slide 119
Chart: 

## Slide 120
Chart: